Cluster I/O Performance On Large Data Files

---
Specifications
Using CMS3 files trimmed to 2GB
Reads compared:
local disk
HDFS through FUSE
ram cache

---
Local Disk Performance

---
Local Disk Performance
1. No files being written to disk
2. Ram cache dropped after each read
Reproduces conditions for proposed babymaking I/O procedure.
Max Read Velocity ~ 100 MB/s from 1 or 3 files with large buffer size.
30% performance hit when reading from 10 files.

---
Local Disk Performance (with write)

---
Local Disk Performance (with write)
1. No files being written to disk
2. Ram cache dropped after each read
3. Continuously writing ~10MB/s to disk
Max Read Velocity ~ 95 MB/s from 1 file, buffer size independent?
30% performance hit when reading from 10 files.

---
Ram Cache Performance

---
Ram Cache Performance
No files being written to disk
Max Read Velocity ~ 6 GB/s from 3, 6, or 10 files independent of buffer size.
50% performance hit when reading from 1 file.

---
HDFS Performance

---
HDFS Performance
1. No files being written to disk
2. No attempt to drop ram cache
3. HDFS mounted through FUSE
Reproduces conditions for current babymaking procedure.
Max Read Velocity ~ 115 MB/s from 6 to 10 files with large buffer size.
50% performance hit when reading from 1 file.

---
Next Steps
Read through HDFS C API if possible
Take HDFS reads when the cache has been dropped
Try reads with files spread over multiple disks on the same machine to test possible CPU or bus-speed bottleneck
Convert babymaking code to read from local disk

---
Conclusions
HDFS read is network limited near 100 MB/s which is approximately equal to the performance of a single drive.
Further testing needed to predict performance increase, but niavely we can expect 10x I/O performance if local disk reads are not bus limited.